## Cost Benefit Analysis - Draft Data Form

# Basin Description

Basin	Spey – Upstream of Boat of Garten

Area (km²)	1272 km²

Location (Lat., Long.)

Elevation Range (m)	200-1300m

Model Used	HBV

Comments (e.g. % layover)	Approximately 30% of catchment is subject to abstraction

Data entered by	Roger Dunham

Date of form completion	9th March, 1999.

# Calibration Stage

-Data costs to set-up the system

Please indicate whether the following data sets were bought in, or derived in house

|  | Bought-in | Derived in-house |
| --- | --- | --- |
| Land cover | x | x |
| Historic runoff | x |  |
| Historic meteorological data | x |  |
| Historic snow cover area |  | x |
| DEM | x |  |
| Sub-catchment boundaries | x |  |
| Model “tuning” |  | x |

# “Tooling up” costs

- hardware and software costs to set-up the system

Please provide descriptive answers for the following questions

| Actual Hardware used |  |
| --- | --- |
| Minimum specification |  |
| Software – model license |  |
| Network |  |
| Personnel training |  |

# Forecasting phase

- costs which will only be incurred if models are used

Please tick whether data is bought in or derived in house

|  | Bought in | Derived in house |
| --- | --- | --- |
| EO data for SCA |  | x |
| Current runoff | x |  |
| Current meteorological data | x |  |
| Model operation |  | x |

# Description of data output

Format of output data	Digital maps of snow covered area. Digital predictions of runoff volume. Exported over Network to Hydro-electric company

Cost of outputting data	Negligible

# “Profit”

% of costs if working as an agency	27%

Calibration Phase – Bought-in data

# Land Cover

| Source of land cover data | MLURI LCS88 |
| --- | --- |
| Data obtained | Land cover polygons in 33 categories. Data available for whole of Scotland. See metadata form: http://bamboo.mluri.sari.ac.uk/hydalp/private/meta_results/dat_chk/basuk_lcs.html |
| Cost (please state whether purchase or lease) | Free to project. Normal cost is £xxxx. Data is leased |
| Was data suitable for use in the form in which it was obtained, without further processing? | No |
| If “No”, then please state what additional processing was required | Data was more complex than required for HBV. Data categories were merged to simplify them. This required 1 man day and 30 minutes CPU time on Sparc Ultra 10 |

# Historic Runoff

| Source of Runoff data | Scottish Environment Protection Agency (SEPA) |
| --- | --- |
| Data obtained | Measurements of Discharge, gauged river level, Mean Daily Flow (MDF), Mean daily runoff or monthly average forecasts for stations relevant to BASUK. Data present for stations: Boat of Garten (1978-97), Feshiebridge (1992-97), Kincraig (1993-97), Tromie Bridge (1978-97) and Loch Seilich (1980-96). See Metadata form: http://bamboo.mluri.sari.ac.uk/hydalp/private/meta_results/dat_chk/basuk_hyd.html |
| Cost (please state whether purchase or lease) | Data free to project. Normal cost is £xxxx |
| Was data suitable for use in the form in which it was obtained, without further processing? | No |
| If “No”, then please state what additional processing was required | Required processing to provide discharge in mm, based on catchment area All files initially in ASCII text format, required conversion to HydAlp data format. |

# Historic meteorological data

| Source of meteorological data | British Atmospheric Data Centre (BADC) WWW site |
| --- | --- |
| Data obtained | Measurements of daily temperature, rainfall and snowfall for stations relevant to BASUK. All in ASCII text files (have to be converted to HydAlp data format). Data from stations Aviemore (1984-1996), Cairngorm Chairlift (1981-1996), Dalwhinnie(1978-1996), Glenlivet (1978-1996), Braemar (1978-1997). See metadata form: http://bamboo.mluri.sari.ac.uk/hydalp/private/meta_results/dat_chk/basuk_met.html |
| Cost (please state whether purchase or lease) | Free to project. Commercial price would be £xxxx |
| Was data suitable for use in the form in which it was obtained, without further processing? | No |
| If “No”, then please state what additional processing was required | Transfer of data to an HBV readable format. (1 hour per station) |

# Historic EO data for Snow Cover

| Source of EO data |  |
| --- | --- |
| Data obtained |  |
| Cost (please state whether purchase or lease) |  |
| Was data suitable for use in the form in which it was obtained, without further processing? |  |
| If “No”, then please state what additional processing was required |  |

# DEM

| Source of DEM | Ordnance Survey |
| --- | --- |
| Data obtained | 1:50,000 and 1:10,000 DEM |
| Cost (please state whether purchase or lease) | Free to project. Normal prices: £40 per 20 x 20 km tile for 1:50,000. £100 per 20 x 20 km tile or 1:10,000. |
| Was data suitable for use in the form in which it was obtained, without further processing? | Yes |
| If “No”, then please state what additional processing was required |  |

# Model “tuning” and verification

| Organisation or individual tuning model. |  |
| --- | --- |
| Cost |  |
| Was tuning suitable for use |  |
| If “No”, then what extra work was required? |  |

Calibration Phase – Data Derived in-house

# Landcover

| Method of deriving land cover – photographs, EO, Field surveys | Unsupervised classification of Landsat TM data |
| --- | --- |
| Input data costs | Landsat TM (26/6/95) image free to project. Commercial price for 90 x 90 km image is £1600 |
| Data preparation costs | Geocoding. 2 man-hours |
| Processing costs | 1 hour CPU time |
| Validation costs | Comparison with independent LCS88 data. 2 man-days |
| Hardware requirements | Sparc Ultra 10 |
| Software requirements | Erdas Imagine used, but PCI would be acceptable. |
| Network requirements | Not used. Image was provided on DAT tape |
| Personnel requirements | Trained in the use of ERDAS Imagine |

# Historic Runoff

| Method of deriving runoff data |  |
| --- | --- |
| Input data costs |  |
| Data preparation costs |  |
| Processing costs |  |
| Validation costs |  |
| Hardware requirements |  |
| Software requirements |  |
| Network requirements |  |
| Personnel requirements |  |

# Historic Meteorological Data

| Method of deriving met. data |  |
| --- | --- |
| Input data costs |  |
| Data preparation costs |  |
| Processing costs |  |
| Validation costs |  |
| Hardware requirements |  |
| Software requirements |  |
| Network requirements |  |
| Personnel requirements |  |

# Historic SCA assessment

| Method of deriving SCA data | SCA data derived from Landsat TM, SAR and AVHRR images, using flowlines developed within HydAlp project. |
| --- | --- |
| Input data costs | Landsat and AVHRR images free to project. Commercial prices are: 1 x Landsat TM image (90 x 90 km) at £1600 5 x SAR images at £600. 12 x AVHRR at £40 |
| Data preparation costs | Geocoding. 1 man hour per image |
| Processing costs | Landsat image 1 CPU hour SAR image 5 CPU hours AVHRR image 0.5 CPU hours |
| Validation costs | SAR and AVHRR derived data compared with TM derived data. No additional data costs. 3 man days. |
| Hardware requirements | Sparc Ultra 10 |
| Software requirements | ERDAS Imagine for Landsat TM and AVHRR. ERDAS Imagine and Radar module for SAR |
| Network requirements | TM and SAR data provided on DAT tape. AVHRR image downloaded via 100Mbps Area Network. Individual files are 40Mb |
| Personnel requirements | Staff trained in use of ERDAS Imagine |

# DEM

| Method of deriving DEM |  |
| --- | --- |
| Input data costs |  |
| Data preparation costs |  |
| Processing costs |  |
| Validation costs |  |
| Hardware requirements |  |
| Software requirements |  |
| Network requirements |  |
| Personnel requirements |  |

# Model tuning and validation

| Method of tuning and validating model | HBV tuned using historic meteorological and runoff data from 1986 to 1995. Validated using data from 1996 to 1998. |
| --- | --- |
| Input data costs | Already noted |
| Data preparation costs | Conversion to HydAlp format ¼ man-hour per met. station. ¼ man-hour per stream gauge. |
| Processing costs | 12 man-weeks and 12 CPU hours |
| Validation costs | 3 man-weeks |
| Hardware requirements | Pentium MMX 233 with 48 Mb RAM |
| Software requirements | HBV |
| Network requirements | Not required |
| Personnel requirements | Staff trained in HBV |

Forecasting Phase – Bought In Data

# NRT Runoff

| Source of Runoff data | Data provided by Hydro-electric companies array of telemetric flow gauges |
| --- | --- |
| Data obtained | Stage in fourteen locations throughout catchment. This can be converted to discharge through known stage/discharge calibration. |
| Cost (please state whether purchase or lease) | Nil to project |
| Was data suitable for use in the form in which it was obtained, without further processing? | No |
| If No then please state what additional processing was required | Required conversion to Hydalp format. This was achieved using an automated script. 30 seconds CPU time required. |

# NRT meteorological data

| Source of meteorological data | UK Meteorological Office |
| --- | --- |
| Data obtained | Daily measurements of temperature and precipitation for recent past, and for ten day forecast, for five stations in or near basin. |
| Cost (please state whether purchase or lease) |  |
| Was data suitable for use in the form in which it was obtained, without further processing? | No |
| If No then please state what additional processing was required | Conversion to hydalp format using automated script. 30 seconds CPU time required |

# NRT Snow Cover

| Source of SCA data |  |
| --- | --- |
| Data obtained |  |
| Cost (please state whether purchase or lease) |  |
| Was data suitable for use in the form in which it was obtained, without further processing? |  |
| If No then please state what additional processing was required |  |

# NRT snowmelt forecasts

| Source of snowmelt data |  |
| --- | --- |
| Data obtained |  |
| Cost |  |
| Was data suitable for use in the form in which it was obtained, without further processing? |  |
| If No then please state what additional processing was required |  |

Forecasting Phase – Data Derived in House

# NRT Runoff

| Method of deriving runoff data |  |
| --- | --- |
| Input data costs |  |
| Data preparation costs |  |
| Processing costs |  |
| Validation costs |  |
| Hardware requirements |  |
| Software requirements |  |
| Network requirements |  |
| Personnel requirements |  |

# NRT Meteorological Data

| Method of deriving runoff data |  |
| --- | --- |
| Input data costs |  |
| Data preparation costs |  |
| Processing costs |  |
| Validation costs |  |
| Hardware requirements |  |
| Software requirements |  |
| Network requirements |  |
| Personnel requirements |  |

# NRT SCA assessment

| Method of deriving runoff data | Data derived from 5 SAR images and 2 AVHRR images |
| --- | --- |
| Input data costs | AVHRR free to project but commercial cost £40. SAR images £600 |
| Data preparation costs | Geocoding. 1 man-hour per image |
| Processing costs | SAR image 5 CPU hours AVHRR image 0.5 CPU hours |
| Validation costs | Validation is not conducted directly. |
| Hardware requirements | Sparc Ultra 10 |
| Software requirements | ERDAS Imagine |
| Network requirements | Data is acquired via ftp. SAR images are 130 Mb AVHRR images are 40 Mb 100 Mbps Wide Area Network used |
| Personnel requirements | Staff trained in ERDAS Imagine |

# NRT snowmelt forecasting

| Method of forecasting snowmelt | HBV |
| --- | --- |
| Input data costs | Meteorological, river gauging and SCA data already accounted for |
| Data preparation costs | Conversion to HydAlp format. Automated script used. ¼ man-hour |
| Processing costs | 5 minutes CPU time |
| Validation costs | Validation is conducted by comparing predictions with observed discharges |
| Hardware requirements | Pentium MMX 233 with 48 Mb RAM 486 would be acceptable. |
| Software requirements | HBV |
| Network requirements | Met. and runoff data must be imported via network. Files typically 48 kb. 100 Mbps WAN used, but modem would be adequate for small files |
| Personnel requirements | Technical assistant trained in use of HBV ½ day per model “run” |

# Footnotes

The specification of hardware which is realistically required.  This could be lower (A Pentium II 400 actually used but a 286 would have been adequate) or higher (you managed, but it was excessively difficult or slow) than what was actually used.

This relates to the external network – i.e. whether data is transferred by modem, WAN etc.

Skills required to perform work. This may vary from task to task, and is requested in more detail on subsequent pages

either or both time or cash values should be included in each category